DN301 Installation Instructions

- Product Confirmation

| DN301 board | M3 screw |
| --- | --- |

- Component Name

| No. | Name | Instructions |
| --- | --- | --- |
| a | Mounting hole | Use M3 screw to install the DN301 board to the inverter |
| b | Connector | Communication connecting terminal |
| c | Connector | Connect to the inverter |
| d | Switch | Switch communication Baud rate(500kbps, 250 kbps, 125 kbps)and station number(0~63) |
| e | Plastic handle | Remove DN301 board |
| f | Terminal resister | Terminal resister switch, the default state is OFF |

- Devicenet Ports Definition

| Terminal | Signal | Description |
| --- | --- | --- |
| V+ | V+ | DC24V |
| CAN+ | CAN+ | Positive Signal wire |
| SH | SHIELD | Ground wire |
| CAN- | CAN- | Complex signal wire |
| V- | V- | 0V |

- Functional Specification

| Item specification | Description |
| --- | --- |
| Power | External power input Input voltage: 24V |
| Standard | Follow ODVA DeviceNet specification 2.0 version (Group 2 Only Device) |
| Network form | DeviceNet (linear bus with branch line) |
| Communication cable | DeviceNet standard thick cable or thin cable (Branch cable should be thin cable.) |
| Maximum cable length | 500m (125kbps) 250m (250kbps) 100m (500kbps) |
| Item specification | Description |
| Communication speed | 125kbps, 250kbps, 500kbps |
| Quantity of connected inverters | 64 (including the main machine) When connecting at least one node as the main machine, the quantity of connected inverters is 64-1 = 63. |

- Devicenet Switch Setting

The default setting of switch SW1 is OFF. When multiple machines are in communication, the switch of DN301 farthest from the position machine should be set as 121Ω. And other SW1 of DN301 stays the factory default state (OFF).

- Installation (SA3)

Step 1：Insert DN301 expansion card to SLOT 1 .DO NOT plug it in SLOT 2 or SLOT 3.

Step 2：Tighten the M3 screws with 4-6kgf.cm torque on the card as figure 2 shown.

Note：

1. For SA3–A frame inverters, remove the plastic part shown in figure 3, the result is shown in figure4.

2. When disassembling DN301, loosen the M3 screws first, and then lift the plastic handle.

Figure 1                                             Figure 2

Figure 3                                 Figure 4

- Installation（SE3）

Step 1：Turn off the power.

Step 2：Open the top Cover of the inverter.

Step 3：Use the front rear as support and slide (a) in by pressing down as figure 1 shown.。

Figure 1

Note: (a)-Optional Card Housing; (b)-Hook, (c)-Slot

Step 4: Line up the connector (c) and (d), and press down the DN301 expansion card to the right position.

Figure 2

（a）(e)-Supporter, (b)-Plastic Handle, (c)-Male connector, (d)-Female connector

Step 5: Tighten two M3 screws with 4-6kgf.cm torque on the card. Install the Cover after wiring.

Figure 3

- Others

(To improve our products, the parameters and contents may be modified, please contact the agent or refer to Shihlin websites

(http://automation.seec.com.tw/) to download the latest version.