Installation Instructions for EP301 Expansion Card

- Product clarification

| EP301 card | M3 screws |
| --- | --- |

- Parts specification

| No. | Name | Description |
| --- | --- | --- |
| a | Mounting hole | Assemble the EP301 expansion card on the inverter with M3 screws |
| b | SPEED LED | Indicates internet speed |
| f | LINK LED | Indicates internet connection |
| c | Plastic handle | For disassembling EP301 expansion card |
| d | RJ45 | Communication slot |
| e | Connector | Connect with inverter |

- Slot specification

| Type | Terminal number | Name | Description |
| --- | --- | --- | --- |
| RJ45 | 1 | Tx+ | +signal output |
|  | 2 | Tx- | -signal output |
|  | 3 | RX+ | +signal input |
|  | 4 | --- | --- |
|  | 5 | --- | --- |
|  | 6 | RX- | -signal input |
|  | 7 | --- | --- |
|  | 8 | --- | --- |

Note：EP301 is only compatible with SA3 version V0.130 or higher

- Installation（SA3）

Step 1：Insert EP301 expansion card to SLOT 1 .DO NOT plug it in SLOT 2 or SLOT 3.

Step 2：Tighten the M3 screws with 4-6kgf.cm torque on the card as figure 2 shown.

Note：

1. For SA3–A frame inverters, remove the plastic part shown in figure 3, the result is shown in figure4.

2.When disassembling EP301,loosen the M3 screws first,then lift the plastic handle.

Figure 1                                       Figure 2

Figure 3                                Figure 4

- Installation（SE3）

Step 1：Turn off the power.

Step 2：Open the top coverof the inverter.

Step 3：Use the front rear as support and slide (a) in by pressing down as figure 1 shown.。

Figure 1

Note: (a)-Optional Card Housing; (b)-Hook, (c)-Slot

Step 4: Line up the connector (c) and (d), and press down the EP301 expansion card to the right position.

Figure 2

（a）(e)-Supporter, (b)-Plastic Handle, (c)-Male connector, (d)-Female connector

Step 5: Tighten two M3 screws with 4-6kgf.cm torque on the card. Install the cover after wiring.

Figure 3

- Other

(To improve our products, the parameters and contents may be modified, please contact the agent or refer to Shihlin websites

(http://automation.seec.com.tw/) to download the latest version.