PG301L Installation Instructions

Product Confirmation

| PG301L board | M3 screw |
| --- | --- |

- Component Name

| No. | Name | Instructions |
| --- | --- | --- |
| a | Mounting hole | Use M3 screw to install the PG301L board to the inverter |
| b | Terminal | Connect wiring for customer |
| c | Connector | Connect to the inverter |
| d | Switch | S stands for standard non-unwire mode encoder, L stands for unwire mode encoder |
| e | Plastic handle | Remove PG301L board |

| Terminal | Terminal Symbols | Function instruction | Terminal specification |
| --- | --- | --- | --- |
| Input | A1、B1、Z1 | The input of the encoder signal supports open collector, voltage, line drive and push-pull input type. | Maximum frequency: 500KP/Sec |
|  | 、、 |  |  |
|  | A2、B2 | The input of pulse signal connects to the upper controller and supports open collector, voltage, line drive and push-pull input type. | Maximum frequency: 500KP/Sec |
|  | 、 |  |  |
| Output | AO、BO、ZO | The line-drive dividing frequency output is 1～255 times dividing frequency. | Maximum output voltage: 5V Maximum current: 50mA Maximum frequency: 500KP/Sec |
|  | 、、 |  |  |
| Power | 12V | 12V Power | Voltage ±5% Current 200mA MAX |
|  | 5V | 5V Power |  |
|  | DCM | Power grounding |  |

- Terminal Description

- Wiring Schematic Diagram

- Precautions

- The shielded wire should be used to prevent interference. Do not line up in parallel when the voltage is 200V or above.

- Recommended wiring size：0.20~1.25mm2 (AWG24~AWG16).

- Length

| Encoder output type | Maximum Length | Wiring Specification |
| --- | --- | --- |
| voltage | 50m | 1.25 mm2(AWG16 and above) |
| open collector | 50m |  |
| line drive | 300m | 1.25 mm2(AWG16 and above) |

- Dividing frequency coefficient is determined by dividing frequency parameter P.357, and the setting range is 0~255. The relationship is as follows:

| P.357 | Dividing frequency coefficient |
| --- | --- |
| 0 | 1 |
| 1 | 2 |
| …… | …… |
| n | n+1 |
| …… | …… |
| 255 | 256 |

- Applying Wiring

6.1 Wiring sketch map of the differential output encoder   6.2 Wiring sketch map of the open collector output encoder

6.3 Wiring sketch map of the push-pull output encoder    6.4 Wiring sketch map of the voltage output encoder

- Installation Instructions

7.1 SA3 Installation

Step1: As the Figure 1 shows, please insert PG301L board into the control board SLOT 2, neither SLOT 1 nor SLOT 3.

Step2: Please lock the two M3 screws with screwdriver according to the torque of 4-6kgf.cm and the direction showed in Figure 2.

Note: When removing PG301L board, please first remove the right and left M3 screws, and then lift the plastic handle by hand.

Figure1                                                     Figure2

7.2 SE3 Installation

Step 1：Turn off the power.

Step 2：Open the top coverof the inverter.

Step 3：Use the front rear as support and slide (a) in by pressing down as figure 1 shown.。

Figure 1

Note: (a)-Optional Card Housing; (b)-Hook, (c)-Slot

Step 4: Line up the connector (c) and (d), and press down the PG301L expansion card to the right position.

Figure 2

（a）(e)-Supporter, (b)-Plastic Handle, (c)-Male connector, (d)-Female connector

Step 5: Tighten two M3 screws with 4-6kgf.cm torque on the card. Install the cover after wiring.

Figure 3                             Figure 4

- Others

(To improve our products, the parameters and contents may be modified, please contact the agent or refer to Shihlin websites

(http://automation.seec.com.tw/) to download the latest version.

# Text boxes

Need Cutout this area for installating the cover