PG302L Installation Instructions

- Product Confirmation

| PG302L board | M3 screw |
| --- | --- |

- Component Name

| No. | Name | Instructions |
| --- | --- | --- |
| a | Mounting hole | Use M3 screw to install the PG302L board to the inverter |
| b | Terminal | Connect wiring for customer |
| c | Connector | Connect to the inverter |
| d | Plastic handle | Remove PG302L board |
| e | L light | Signal loss |
| f | D light | Signal degradation |
| g | Power light | Power instruction |
| h | A, B, Z light | A, B, Z signal light |

- Terminal Description

| Name | Description |
| --- | --- |
| Power | Supplied by the noumenon R1-R2 excitation source 7Vrms, 10KHz |
| Input terminal | Rotary transform S1，S2 input 3.5±0.175Vrms, 10KHz A2, , B2, : The input of pulse signal connects to the upper controller and supports open collector, voltage, line drive and push-pull input type. The maximum is 500K. |
| Name | Description |
| Output terminal | AO, , BO, , ZO, : The line-drive dividing frequency output is 1～255 times dividing frequency, the maximum output current is 50mA, output voltage is 5V, and the maximum output frequency is 500K. |

- Wiring Schematic Diagram

- Precautions

- The shielded wire should be used to prevent interference. Do not line up in parallel when the voltage is 200V or above.

- Recommended wiring size: 0.20~1.25mm2 (AWG24~AWG16).

- PG board dividing frequency coefficient is determined by dividing frequency parameter P.357, and the setting range is 1~255. The relationship is as follows:

| P.357 | Dividing frequency coefficient |
| --- | --- |
| 1 | 1 |
| 2 | 2 |
| …… | …… |
| n | n |
| …… | …… |
| 255 | 255 |

Note: Parameter P.357 is the multiple setting for PG board feedback and output. If the feedback is 1024PPR, the setting of P.357 is “2”, and the PG OUT (pulse output) is 512PPR.

- When using PG302L feedback motor rotation speed, the corresponding setting parameters are from P.350 to P.354; if using A2/B2 input pulse signal, the corresponding setting parameters are P.355/P.356. Besides, P.350 should be set to 1024. For the setting mode of P.351~P.356, please refer to SA3 User Manual.

- Applying Wiring

Line-drive Output Wiring Diagram

- Installation Instructions

7.1 SA3 installation

Step1: As the Figure 1 shows, please insert PG302L board into the control board SLOT 2, neither SLOT 1 nor SLOT 3.

Step2: Please lock the two M3 screws with screwdriver according to the torque of 4-6kgf.cm and the direction showed in Figure 2.

Note: When removing PG302L board, please first remove the right and left M3 screws, and then lift the plastic handle by hand.

\

Figure 1                                         Figure 2

7.2 SE3 Installation

Step 1：Turn off the power.

Step 2：Open the top coverof the inverter.

Step 3：Use the front rear as support and slide (a) in by pressing down as figure 1 shown.

Figure 1

Note: (a)-Optional Card Housing; (b)-Hook, (c)-Slot

Step 4: Line up the connector (c) and (d), and press down the PG301L expansion card to the right position.

Figure 2

（a）(e)-Supporter, (b)-Plastic Handle, (c)-Male connector, (d)-Female connector

Step 5: Tighten two M3 screws with 4-6kgf.cm torque on the card. Install the cover after wiring.

Figure 3                             Figure 4

8. Others

(To improve our products, the parameters and contents may be modified, please contact the agent or refer to Shihlin websites

(http://automation.seec.com.tw/) to download the latest version.

# Text boxes

Need Cutout this area for installating the cover