PG301C Installation Instructions

- Product Confirmation

| PG301C board | M3 screw |
| --- | --- |

- Component Name

| No. | Name | Instructions |
| --- | --- | --- |
| a | Mounting hole | Use M3 screw to install the PG301C board to the inverter |
| b | Terminal | Connect wiring for customer |
| c | Connector | Connect to the inverter |
| d | Switch | S stands for standard non-uniwire mode encoder, L stands for uniwire mode encoder |
| e | Plastic handle | Remove PG301C board |

- Terminal Description

| Terminal | Terminal Symbols | Function instruction | Terminal specification |
| --- | --- | --- | --- |
| Input | A1、B1、Z1 | The input of the encoder signal supports open collector, voltage, line drive and push-pull input type. | Maximum frequency: 500KP/Sec |
|  | 、、 |  |  |
|  | A2、B2 | The input of pulse signal connects to the upper controller and supports open collector, voltage, line drive and push-pull input type. | Maximum frequency: 500KP/Sec |
|  | 、 |  |  |
| Output | A1O | The open collector dividing frequency output is 1~255 times dividing frequency. The maximum output current is 50mA. | Maximum frequency: 500KP/Sec, Maximum current: 50mA It can switch pull-up resistors under different voltages. |
|  | B1O |  |  |
|  | Z1O |  |  |
|  | DCM |  |  |
| Power | 12V | 12V Power | Voltage ±5% Current 200mA MAX |
|  | 5V | 5V Power |  |
|  | DCM | Power grounding |  |

- Wiring Schematic Diagram

- Precautions

- The shielded wire should be used to prevent interference. Do not line up in parallel when the voltage is 200V or above.

- Recommended wiring size：0.20~1.25mm2 (AWG24~AWG16).

- Length

| Encoder output type | Maximum Length | Wiring Specification |
| --- | --- | --- |
| voltage | 50m | 1.25 mm2(AWG16 and above) |
| open collector | 50m |  |
| line drive | 300m | 1.25 mm2(AWG16 and above) |
| compensation | 70m |  |

- If the dividing frequency signal is connected to the user power, the voltage should be lower than 24V in series with current-limiting resistance(refer to the recommended specification in the following table), otherwise PG301C board will be damaged.

| 5V | Recommended pull-up resistor: 330~510Ω，1/2W以上 |
| --- | --- |
| 12V | Recommended pull-up resistor: 510~1.35kΩ，1/2W以上 |
| 24V | Recommended pull-up resistor: 1.8k~3.3kΩ，1/2W以上 |

- Dividing frequency coefficient is determined by dividing frequency parameter P.357, and the setting range is 0~255. The relationship is as follows:

| P.357 | Dividing frequency coefficient |
| --- | --- |
| 0 | 1 |
| 1 | 2 |
| …… | …… |
| n | n+1 |
| …… | …… |
| 255 | 256 |

- Applying Wiring

6.1 Wiring sketch map of the differential output          6.2 Wiring sketch map of the open collector output

encoder                                          encoder

6.3 Wiring sketch map of the push-pull output          6.4 Wiring sketch map of the voltage output

encoder                                         encoder

6.5 The open collector dividing frequency output connection diagram   PG301C

- Installation Instructions

7.1 SA3 installation

Step1: As the Figure 1 shows, please insert PG301C board into the control board SLOT 2, neither SLOT 1 nor SLOT 3.

Step2: Please lock the two M3 screws with screwdriver according to the torque of 4-6kgf.cm and the direction showed in Figure 2.

Note: When removing PG301C board, please first remove the right and left M3 screws, and then lift the plastic handle by hand.

Figure 1                                          Figure 2

7.2 SE3 Installation

Step 1：Turn off the power.

Step 2：Open the top coverof the inverter.

Step 3：Use the front rear as support and slide (a) in by pressing down as figure 1 shown.

Figure 1

Note: (a)-Optional Card Housing; (b)-Hook, (c)-Slot

Step 4: Line up the connector (c) and (d), and press down the PG301C expansion card to the right position.

Figure 2

（a）(e)-Supporter, (b)-Plastic Handle, (c)-Male connector, (d)-Female connector

Step 5: Tighten two M3 screws with 4-6kgf.cm torque on the card. Install the cover after wiring.

Figure 3                             Figure 4

- Others

(To improve our products, the parameters and contents may be modified, please contact the agent or refer to Shihlin websites

(http://automation.seec.com.tw/) to download the latest version.

# Text boxes

Need Cutout this area for installating the cover