Installation Instructions for CP301 Expansion Card

- Product Confirmation

| CP301 card | M3 screws |
| --- | --- |

- Component Name

| No. | Name | Description |
| --- | --- | --- |
| a | Mounting hole | Assemble the CP301 expansion card on the inverter with M3 screws |
| b | Connector | For connecting to the inverter |
| c | Switch | The terminal resister switch, the default state is Open |
| d | Plastic handle | For disassembling CP301 expansion card |

- RJ-45 Pin Definition

| Pin | Symbol | Description |
| --- | --- | --- |
| 1 | CAN_H | CAN_H bus line (dominant high) |
| 2 | CAN_L | CAN_L bus line (dominant low) |
| 3 | CAN_GND | Ground/0V/V- |
| 7 | CAN_GND | Ground/0V/V- |

Socket

- Function and Specification

| Connector | RJ-45 |
| --- | --- |
| Port | 2 Port |
| Transmission mode | CAN |
| Transmission cable | Using CAN standard line |
| Transmission rate | 1M 500k 250k 125k 100k 50k |
| Protocol | CANopen Protocol |

- CANopen Communication Wire

Type: SNKCBLxxGTNA (xx stands for 1R5, 3, 5, 10)

| Item No. | Part No. | L(mm) |
| --- | --- | --- |
| 1 | SNKCBL1R5GTNA | 1500 |
| 2 | SNKCBL3GTNA | 3000 |
| 3 | SNKCBL5GTNA | 5000 |
| 4 | SNKCBL10GTNA | 10000 |

- CANopen Switch Setting

The default setting of switch SW1 is OPEN. When multiple inverters are in communication mode, the CP301 card on the inverter with the longest distance to the position machine should be switch to 120Ω, and keep other SW1 setting of CP301 default(OPEN).

- Installation (SA3)

Step 1：Insert CP301 expansion card to SLOT 1 .DO NOT plug it in SLOT 2 or SLOT 3.

Step 2：Tighten the M3 screws with 4-6kgf.cm torque on the card as figure 2 shown.

Note：

1. For SA3–A frame inverters, remove the plastic part shown in figure 3, the result is shown in figure4.

2.When disassembling CP301, loosen the M3 screws first, then lift the plastic handle.

Figure 1                                             Figure 2

Figure 3                                 Figure 4

- Installation（SE3）

Step 1：Turn off the power.

Step 2：Open the top Cover of the inverter.

Step 3：Use the front rear as support and slide (a) in by pressing down as figure 1 shown.。

Figure 1

Note: (a)-Optional Card Housing; (b)-Hook, (c)-Slot

Step 4: Line up the connector (c) and (d), and press down the CP301 expansion card to the right position.

Figure 2

（a）(e)-Supporter, (b)-Plastic Handle, (c)-Male connector, (d)-Female connector

Step 5: Tighten two M3 screws with 4-6kgf.cm torque on the card. Install the Cover after wiring.

Figure 3

- Others

(To improve our products, the parameters and contents may be modified, please contact the agent or refer to Shihlin websites

(http://automation.seec.com.tw/) to download the latest version.